Data Structures:

Three dimensional vector class, implicit support for operations with scalars */ and vector to vector operations +- and dot product

3x3 Square matrix, support for implicit multiplication with 3x1 vectors or 3x3 Matrices as well as static matrix operations such as the determinant, transpose, cofactor, minor, inverse, and a constructor that can take an x rotation and y rotation and form a rotation matrix. (and the inverse of that)

Body class, describes necessary attributes of any body in the system, including standard gravetational parameter, position, velocity, radius, luminosity and reflectivity.

PlanetarySystem class, includes a list of the bodies along with a vector describing the bounds of the system (from negative to positive)

Plane class, describes a plane in the form %PI = M( %lambda i + %mu j ) + ck , with M and c defined

Algorithms:

GetAcceleration(PlanetarySystem):
returns a list of the instantaneous acceleration of each body, using Newton's laws
1. generate zero array of length number of bodies
2. recurse through all pairs of bodies, finding force*G, GM*Gm/r^2
3. add acceleration , F/GM (GM is stored in the body) to each relevant element

TimeStep(PlanetarySystem, acceleration, step):
applies the acceleration to the planetary system and calculates velocity and position,
assuming constant acceleration, for the given step (in s).
1. Iterate through bodies and acceleration
2. Add acceleration*step to velocity
3. Add 1/2 * a * t^2 to position
ReflectionPlanes(luminous body,PlanetarySystem):
returns the plane of reflection of each body in the PlanetarySystem from the luminous body.
This refers to the hemisphere that light reaches.
VisiblePlanes(position vector of observer, PlanetarySystem):
returns the plane through each body to which the
vector between the observer and the centre is normal.
Color(PlanetarySystem):
Finds the average color of each body
Draw(reflection planes, visible planes, colors):
converts the results of the last three algorithms into a 2D array to be drawn to the screen
Display(bitmap):
Handles display output, including GUI

click handling, need to research